## Slide 1: Wind Speed Data Logger Chuck Craft, Chuck Craft., Jr., Professor Paul I-Hai Lin Date: Sept. 20-23, 2012

## Slide 2: Project Outline
Introduction
Problem Statement/Solution
System design
Hardware design
Software design
Integration
testing
Conclusion

## Slide 3: Introduction
Wind Speed Data Logger project supports the renewable energy market
Large wind generator installations are located in Indiana and Ohio
Average wind speed site surveys predict wind generator return on investment
Test towers erected at potential wind generator sites to gauge average wind conditions
Residential wind generator installations have the potential to be profitable
Wind speed data logger project provides affordable tool for residential wind survey

## Slide 4: Problem Statement/Solution
Viable wind energy exists in our area
Wind generator output power is dependent on
  Structures
  Site topology
Industrial wind survey equipment is expensive
Wind speed data logger provides affordable easy to use tool for residential wind survey

## Slide 5: System Design
Anemometer
End point controller
Access point controller
Data logger controller

## Slide 6: System Requirements
The prototype shall measure wind speed
The prototype shall transfer wind speed information from sensor to data logging device
The prototype shall store wind speed information in non-volatile memory
The prototype shall accept operator input and display wind speed
The prototype shall be capable of measuring wind speeds between 5 and 50 miles per hour

## Slide 7: System requirements (Cont.)
The anemometer output shall be electrically conditioned to logic levels
The pulse stream from the anemometer shall be converted to one pulse per second at a wind velocity of 2.5 miles per hour
The anemometer shall be designed for pole mounting
Outdoor based electronics shall be mounted in an enclosure
The electronics shall operate off of standard household AC power
Information shall be transferred from the anemometer to a processing element via a data link, either cabled or RF

## Slide 8: Hardware Design
Commercial Off The Shelf (COTS)building blocks
  Vortex anemometer
  Texas Instruments eZ430 evaluation module
  Atmel AVR32 EVK1100 development module
  RS232 adaptor

## Slide 9: Hardware Design (Cont.) Vortex Anemometer Specifications
Sensor type
  3-Cup rotor reed switch/magnet provides 1 pulse per rotation
Output
  1 pulse per rotation at 2.5 mph
Rotor diameter
  Approximately 5 inches
Speed range
  Approximately 3 mph to 125+ mph

## Slide 10: Hardware Design (Cont.) eZ430 Module Specifications
MSP430F2274
  16-bit RISC architecture
  Internal calibrated oscillator
  16-bit timers A and B with capture/compare registers
  UART
CC2500
  2.4 GHz to 2.4835 GHz output
  +1 dBm output level (~1.3mW)
  Multiple modulation formats
  SPI digital interface

## Slide 11: Hardware Design (Cont.) EVK1100 Development Module Specifications
AT32UC3A0512 processor
  32-bit RISC architecture
  Real Time Operating System (RTOS)
  512 Kbytes Flash memory
Peripherals
  RS232 (x2)
  USB
  LCD
  Ethernet
  Secure Digital memory slot

## Slide 12: Hardware Design (Cont.) RS232 to TTL Adaptor Module Specifications
MAX232A device from Maxim-ic
  Logic level serial data receive and transmit pins
  RS232 level serial receive and transmit pins
  0.1” center stakes for logic signal connection to custom circuit board
  Standard 9-pin D connector for RS232 cable connection

## Slide 13: Hardware Design (Cont.) End point controller Construction
Custom built module
  eZ430 module
  6 VDC to 40 VDC input, 3.3 VDC output linear regulator circuit
  Anemometer cable termination circuit
  Power indicator LED
  Terminal blocks for external power supply and anemometer connections

## Slide 14: Hardware Design (Cont.) End point controller Schematic

## Slide 15: Hardware Design (Cont.) Access point controller Construction
Custom built module
  eZ430 module
  6 VDC to 40 VDC input, 3.3 VDC output linear regulator circuit
  6 VDC to 40 VDC input, 5.0 VDC output linear regulator circuit
  Power indicator LED (x2)
  Terminal block for external power
  TTL to RS232 adaptor module

## Slide 16: Hardware Design (Cont.) Access point controller Schematic

## Slide 17: Software Design Overview
End point controller function
  Join radio network as end point
  Measure anemometer and calculate wind speed
Access point controller function
  Control radio network as access point function
  Receive information from all end point controllers and send to data logger
Data logger function
  Provide UART shell interface to allow access to display and SD memory peripherals
Software design tools
  Code Composer Studio v4
  AVR Studio 5.0

## Slide 18: Software Design (Cont.)
SimpliciTI network protocol
Five command API

## Slide 19: Software Design (Cont.) End Point Controller

## Slide 20: Software Design (Cont.) End Point Controller Data Processing

## Slide 21: Software Design (Cont.) Access Point Controller

## Slide 22: Software Design (Cont.) Data Logger Controller
Real Time Operating System (RTOS) example program
Shell tasks provided for UART, Ethernet, and USB ports
Modified memory control task to include system time on memory append command
Four commands used by access point to control data logger
  Write string to LCD line four
  Select drive B (SD memory module)
  Append string to log file
  ^q (exit append and save file)

## Slide 23: Integration
Pole assembly constructed from inch PVC pipe
Exterior electrical box included for end point electronics

## Slide 24: Integration (Cont.)
Anemometer mounted to top of pole with cable coiled inside top section of pipe
End point electronics module and power adaptor located in center box

## Slide 25: Integration (Cont.)
Access point controller connected to data logger module
Null modem adaptor used to reverse transmit and receive signals

## Slide 26: RF Subsystem Testing
Signal generator used to emulate anemometer input signal
Testing from 5 mph to 50 mph in 5 mph steps indicated a maximum error of 0.4 mph

## Slide 27: System Testing
System installed in outdoor location for 6 days
Unit ran continuously through rain and cold weather
Recorded 90,225 data entries during test
Log file size at end of test was 4,848 Kbytes
Example data from log file
  EP 1, TEMP = 60.4 F,RSSI = 016, WS = 00.0 mph201203242137000
  EP 1, TEMP = 61.1 F,RSSI = 017, WS = 02.9 mph201203242137000
  EP 1, TEMP = 60.4 F,RSSI = 017, WS = 03.2 mph201203242137000
  EP 1, TEMP = 60.4 F,RSSI = 017, WS = 03.2 mph201203242137000
  EP 1, TEMP = 60.4 F,RSSI = 016, WS = 03.3 mph201203242138000
  EP 1, TEMP = 60.4 F,RSSI = 016, WS = 02.8 mph201203242138000
  EP 1, TEMP = 61.1 F,RSSI = 017, WS = 00.0 mph201203242138000
  EP 1, TEMP = 60.4 F,RSSI = 015, WS = 02.9 mph201203242138000

## Slide 28: System Testing (Cont.)
6 day test data plotted using Microsoft Excel

## Slide 29: Conclusion
Project exceeded all requirements
Completed on time and under budget
Future versions could eliminate EVK1100 module to save money

## Slide 30: Questions?

## Slide 31: Demonstration