## Slide 1: CPET 499/ITC 250 Web Systems
Week 1
Web System Infrastructure, Protocols, and Applications
Paul I-Hai Lin, Professor
Dept. of Computer, Electrical, and Information Technology
College of Engineering, Technology, and Computer Science
http://www.etcs.ipfw.edu/~lin

## Slide 2: Topics
The Internet: Technology Background
  Internet, Web, Packet Switching, TCP/IP Architecture, IP Addresses; Domain Names, DNS, and URLs; Client/Server Computing
TCP/IP Protocols and Application Programs
The New Client: Mobile Platforms
Internet Network Architecture
Internet Service Providers
Internets, Extranet, Wi-Fi, Wireless, Internet 2, etc.
Cloud Computing
Mobile Cellular Networks, IoT

## Slide 3: Topics
The Development of Web
  Web pages - Markup Languages: HTML, XML
  E-mail, Instant Messaging
  Search Engine
  Online Forums and Chat
  Streaming Media
  Cookies
Web 2.0 and Services
  Podcasting, Wikis, Music and Video Services, VoIP, IPTV, Online software, Web Services
Mobile Apps

## Slide 4: Internet
Internet
  A TCP/IP networked, distributed information system
  A collection of computer networks spread around the world
  The name for a group of worldwide client/server-based information system for sharing resources and for communications
  A global, interactive, dynamic, cross-platform, distributed, hypertext and hypermedia information system
Examples of Internet-enabled Services
  Email, File downloading and uploading, WWW Client/Server applications

## Slide 5: Computer Networking & Communications
Examples of Data and Information:
  Voice
  Multimedia
  Video
  Medical record
  Images
  Web pages
  Document
  etc

## Slide 6: Internet
A collection of LANs, WiFi, and WANs systems and network enabled devices and/or computers
Standard Protocols and Applications

## Slide 7: Networking
Involves
  Applications
  Connections of Computers
  Networking Protocols
  Transmission Media
  Networking Devices

## Slide 8: Computer Networks & Distributed Computer Systems
Distributed Processing
  Loosely connected computer networks
  Many computers collaborating with each other
  Client-Server

## Slide 9: Local Area Networks

## Slide 10: Multipoint Line Configuration
Multi-drops
Sharing a single link:
  Spatially
  Time sharing

## Slide 11: Wide Area Networks (WANs)

## Slide 12: TCP/IP Protocol Suite
TCP/IP (Transmission Control Protocol/Internetworking Protocol) Layering Model
TCP/IP Applications
Domain Names
TELNET
FTP (File Transfer Protocol)
HTTP (HyperText Transfer Protocol)
HTTPS (secure)
And more

## Slide 13: Internet Applications and Addressing
Email addressing
Web server addressing (domain name, IP address)
TELNET addressing (Web)
FTP address

## Slide 14: Internet Content/File Types
Email text
HTML (Hypertext Markup Language) document
Hypertext -- a technique used to link one word or phrase to another word or phrase in a virtual digital publishing system
Hypermedia -- a technique used in the Web documents to link one media to another media in the forms of words, color graphics, video clip, etc

## Slide 15: Internet Content/File Types
RTF (Rich Text) - a super ASCII format established by Microsoft in 1980, can be imported to many other systems such as all Windows word processors, and Macs.
Postscript - a highly sophisticated and precise page description language that is used for formatting and typesetting the print media. It is a proprietary format owned by Adobes

## Slide 16: Internet Content/File Types
MIME (Multipurpose Internet Mail Extension) for sending binary data
Color Graphics File
  GIF – Graphics Interchange Format
  JPEG – Joint Photographic Experts Group
Video – Digital motion video
  .mov – QuickTime Movie (plug-in player)
  .avi – Audio/Video Interleaved (1992, Microsoft)
  .mpg – a multimedia standard supporting video, audio, and streaming by Moving Picture Expert Group
Embedded Programs: JavaScript, Java Applet

## Slide 17: Internet Content/File Types
Audio File formats:
wav – Waveform Audio File for PC (uncompressed, CD-quality sound file)
mp3 – the MPEG Layer 3 format (Moving Picture Experts Group)
aiff – Audio Interchange File Format for the MAC
avi – Audio, Video Interleaved
au – standard audio file format used by Sun, Unix and Java
midi: Music Instrument Digital Interface, non-streaming audio file
Real Audio/Video (not-in-real-time audio/ video) - steaming audio/video

## Slide 18: Enterprise Applications
E-commerce
  high availability and security
Messaging/Groupware
Content monitoring
Security
Network Management
Servers:
  Web server
  File and Print server
  Database server
  Mail server

## Slide 19: Enterprise Applications
Intranet:
  A network within an enterprise uses TCP/IP, HTTP, and other Internet protocols
Extranet:
  A private secure extension of an enterprise via a corporate intranet that allows you and your customer, vendors, and other business partners to communicate and do business using standard Internet technology.
Virtual Private Network (VPN)
  A private network uses public telecommunication infrastructure. Privacy is maintained by the use of tunneling protocol, encryption, and other security procedures.

## Slide 20: Internet Web-Enabled Applications
E-Commerce: B2C (Business to Customer), B2B (Business to Business)
E-Health
Smart Power Grid
Electronics publishing with multimedia technology
Database applications
Application Service Provider
Customer Relationship Management (CRM)
Supply Chain Management (SCM)
Enterprise Management (ERP)
Connected smart infrastructure (smartphone, IoTs, smart cities, etc)

## Slide 21: Internet Web-Enabled Applications
Distance Education
Email/Messaging
Teleconferencing
Entertainment
Content Delivery/Advertisement
Machine Control and Monitoring
Cloud-based Services

## Slide 22: TCP/IP Layer Model
Five Layers (Encapsulation of data units)
  Layer 5: Application Layer
    Message
  Layer 4: Transport Layer
    Segment or User Datagram
  Layer 3: Network Layer
    Datagram
  Layer 2: Frame
    Data Link Layer
  Layer 1: Physical Layer
    Bits

## Slide 23: TCP/IP and Internet
Internet
  A virtual network system that is formed by using routers to connect physical networks around the world
Routers
  Special purpose computers dedicated to interconnecting heterogeneous networks
Internet Activities Board (IAB)
  The Internet Engineering Task Force (IETF)
  The Internet Research Task Force (IRTF)
  Request For Comments (RFC) process
  Proposed Standard - Draft Standard - Full-fledged Standard
  http://www.w3.org

## Slide 24: Layered Tasks
Sender, Receiver, and Carrier
Hierarchy
  Preparation
  Sending
  Delivering
Services
  Higher layer uses lower layer service

## Slide 25: TCP/IP Applications
Ping (echo service)
Telnet (RFC 854)
  Remote Login terminal emulation protocol that enable clients to log on to remote hosts on the network
  Provide access to a computer connected to the network
FTP – File Transfer Protocol, (RFC 959)
  RFC 959
  File transfer applications that enables users to transfer files between hosts across network
  Provides two virtual connections:
    Data transfer or exchange (port 20, TCP)
    Control (commands, replies, process updates; port 21, TCP)
SMTP (Simple Mail Transfer Protocol, RFC 821)
  Mail service

## Slide 26: TCP/IP Applications
SNMP (Simple Network Management Protocol)
  RFC 821
  Simple Network Management Protocol) - used to remotely manage and monitor network devices
DNS (Domain Name Services) - domain names to IP address translation

## Slide 27: TCP/IP Applications
HTTP (HyperText Transfer Protocol)
  Establish a connection between the client and server
  For transferring hypertext (mixed media) documents through WWW
  Use TCP/IP to support communications between Web servers and Web clients
  HTTP Communications:
    A Request from a Web client (client  Server)
    A Response from the Web server (server  client)
    Close or terminate the connection

## Slide 28: TCP/IP Applications
NFS (Network File System) - File Access Protocol
POP (Post Office Protocol)
Network News Transfer Protocol
RPC (Remote Procedure Call) - Transfer Procedure (function) Call to another machine
TFTP (Trivial File Transfer Protocol))

## Slide 29: Transport Layer
Transport Layer
  Specify how to ensure reliable transfer
  Defines two protocols
    Transmission Control Protocol (connection oriented, reliable)
    User Datagram Protocol (connectionless, not reliable)

## Slide 30: Domain Names
Human-friendly reference names associated with IP address
For TCP/IP based network system
Standardized in hierarchical fashion
An example:
  www.purdue.edu
  edu - Top level domain name
  purdue - main or network specific domain name
  www - Web server

## Slide 31: Domain Name System (DNS)
DNS identifies each host on the Internet
Similar to the Telephone Number System (country code, area code, number)
A Name Server using Client-Server model
Tree Structure (Root, Leaves):
  Organization (Generic) domain
  Country domain
  Reverse
Unique Domain Name  Unique IP address

## Slide 32: Domain Organization
ICANN (Internet Corporation for Assigned Names and Numbers), http://www.icann.org/
  The authority governs global Internet domain name system
  com Commercial Organization
  edu Educational Institution
  gov Government Institution
  int International Organization
  mil Military Groups
  net Network Support Center
  org Non-profit Organizations
  gTLD (Generic Top-Level Domain) Program, http://www.icann.org/en/registries/

## Slide 33: Domain Organization
November 16, 2000: ICANN, the authority that governs global Internet domain name system, has approved seven new domains extensions, in addition to .com, .net and .org:
biz, info, name, pro, aero, coop, museum
New gTLD (Generic Top-Level Domains), http://newgtlds.icann.org/en/
  Overview (Video), http://newgtlds.icann.org/en/announcements-and-media/video/overview-en

## Slide 34: Summary