## Slide 1: IEEE Fort Wayne Section Technical Presentation April 22, 2014 Indiana University-Purdue University Fort Wayne Room ET 246
Wired and Wireless Sensor Networks for Bridge Health Monitoring
Paul I-Hai Lin, MengWei Li*, Robert Tilbury**, Max Yen, Dong Chen,
*Graduate of Purdue M.S. in Technology ** Graduate student of Purdue M.S. in Technology program
College of Engineering, Technology, and Computer Science
Indiana University-Purdue University Fort Wayne
http://www.etcs.ipfw.edu/~lin

## Slide 2: Wired and Wireless Sensor Network for Bridge Health Monitoring
Topics of Discussion
Overview
The Army/IPFW Corrosion Monitoring System (CMS) Architecture and System Design
The Deployed Army/IPFW CMS System
The CMS System and Communication Subsystem Reliability Issues
Designed and Implemented Communication Infrastructure Improvement
SaaS Cloud Service, and Cloud Storage
Conclusion

## Slide 3: Overview
The project: “Micro-Nano Technology Sol-Gel Corrosion Monitoring System,” 2011-2013
  Project sponsor: Army Construction Engineering Research Laboratory, IL: Richard Lampo and Michael McInerney
  Project Team
    Principal Investigator: Max S. Yen
    Co-Pis: Paul I-Hai Lin and Dong Chen
    Graduate Students: MengWei Li, Robert Tilbury, Muhammad Shoaib Mansur
    Undergraduate EE Student: Steve Groff

## Slide 4: Overview (continue)
The Accomplishments
  “Examination of Corrosion on Steel Structures by Innovative Nano Sol-Gel Sensors,” by Max Yen, Dong Chen, Paul Lin, Bakul Dave, Steve Groff, Emily Hauter, Richard Lampo, and Michael McInerney, NCAE 2012 Corrosion Conference, to be held on March 11-15, 2012, Salt Lake City, Utah
  “Corrosion Sensor for Monitoring Early-Stage Environmental Corrosion of Steel Structure,” Dong Chen, Max yen, and Paul Lin, U.S. Provisional Patten Application #61763523, Feb. 2013
  “Micro-Nano Technology Sol-Gen Corrosion Monitoring System,” New Tech Showcase Demo & Presentation, Indiana University-Purdue University Fort Wayne, April 24, 2013.
  “A Corrosion Monitoring System for Early-Stage Warming of Environmental Corrosion of Structures and Infrastructures,” Technology Showcase, at 2013 Taipei International Invention Show & Technomart, Sept. 26-29, 2013.

## Slide 5: System Architectures of Corrosion Monitoring System: Initial Design (Nov. 2011)
Wireless Sensor Nodes powered by solar panels, with Internet Gateway for Remote Access

## Slide 6: IPFW/Army CMS System Architecture Version 1: Wireless Sensor Nodes, with Internet Gateway (Nov. 2011)
Not implemented due to the concerns of wireless signal interference from other deployed sensor monitoring system

## Slide 7: The IPFW/Army Corrosion Monitoring System Deployed at RIA Bridge, Rock Land, IL
Designed CMS monitoring system architecture
Designed and built Sol-gel, Cylindrical, uncoated and coated with tar-coal epoxy.
Designed and built the analog signal processing circuits for Sol-Gel based sensors and cylindrical sensors
Designed and built the RS-485-based DAQ sensors boxes and cabling system
Completed the testing and installation of CMS at IPFW
Installed the CMS system at Army Rock Island Arsenal Bridge, Rock Island, IL, May 2013
Encountered problems in the areas of Internet Networking and Communication, and followed up with solutions that we will be discussed …

## Slide 8: The IPFW/Army Corrosion Monitoring System
A Windows XP embedded computer: RS-485, Ethernet ports
  DC 12-24V powered, diskless, central controller and data server
  Thermaelectric cooler
  Running the program with “Centralized Data Polling Algorithm” to collect data from six sensor nodes at 30 minutes fixed interval, with time stamp data

## Slide 9: The IPFW/Army Corrosion Monitoring System
Six RS-485-based Sensor Nodes
  DC 24V, ±12V, Power Source
  Microcontroller-based with built-in commands, 12-bit ADC
  Analog signal processing circuits, calibrated for four types of corrosion sensors
Sensor wiring socket
Power and Communication Socket

## Slide 10: The IPFW/Army Corrosion Monitoring System
Six RS-485-based Sensor Nodes
  S1, S2: Coal-tar Epoxy Coated Sol-Gel Sensor
  S3, S4: Sol-Gel Sensor
  S5: Stainless Steel Cylindrical Sensor (coal-tar epoxy coated)
  S6: A36 Cylindrical Sensor (coal-tar epoxy coated)

## Slide 11: The IPFW/Army Corrosion Monitoring System
The Assembled Corrosion Monitoring System in an weather proofed enclosure and 100 ft to 150 ft cables and connectors
Army Sensors
S1 S2 S3
Army Sensors
S4 S5 S6
Power Cable
Internet

## Slide 12: The IPFW/Army Corrosion Monitoring System: Sensor Locations

## Slide 13: The IPFW/Army Corrosion Monitoring System: Sensor Locations

## Slide 14: Installed Cloud Services
The following cloud services were installed on IPFW/Army CMS system, at RIA bridge, Rock Island, IL on May 2013:
  The LogMeIn Hamachi: SaaS (Software as a Service), On Demand Network Virtualization
  LogMeIn Pro: SaaS, remote access to computers for files, applications, and backup service
  DropBox – Cloud Storage Service
    Stored data & files are encrypted, and
    Kept securely on storage service via Amazon’s S3 storage (Simple Storage Service)

## Slide 15: Features of LogMeIn SaaS Cloud Service
LogMeIn Pro, SaaS Cloud Service, Supporting Features
  Remote Access
  Web-based User Interface
  User management
  Computer search
  Online/Offline status
  Reporting
  256-bit SSL encryption
  Audit logging
  Computer grouping
  Host configuration
  Advanced reporting and analysis
  etc

## Slide 16: The LogMeIn – SaaS Cloud Service

## Slide 17: The Windows XP Embedded Data Server: Remotely Accessed through LogMeIn – SaaS Cloud Service

## Slide 18: Dropbox - Cloud Storage Service
All sensor data collected in a 30 minutes interval at Rock Island Arsenal bridge.
Automatically saved into Dropbox storage setup at Embedded computer/data server.
These data saved in Dropbox storage is also synchronized and available to the real-time sensor data processing and web display system setup at IPFW.

## Slide 19: The IPFW/Army CMS Issues and Solutions: First Problem
The installed corrosion monitoring system was successfully collecting data from May 24-26, 2013; then it was offline from May 26 for 1 day, and then was offline since May 29.
  Need to install an UPS for the corrosion monitoring system to ensure the system’s reliability. (added)
  Suspected that high inrush current trip the circuit breaker (replaced with one with high current rating)

## Slide 20: The IPFW/Army CMS Issues and Solutions: First Problem
The installed corrosion monitoring system was successfully collecting data from May 24-26, 2013; then it was offline from May 26 for 1 day, and then was offline since May 29.
  Need to install a remote computer starter to ensure that the corrosion system can be restarted remotely.
    Readjust BIOS Power Management Setting of the Windows XP embedded data server: “Power Lost Resume Control – Turn on”
    iBoot remote starter was tested at IPFW, but not able to function properly due to the fact that a static IP is not available from its current ISP

## Slide 21: The IPFW/Army CMS’s Networking Subsystem Improvement: Successfully Tested at IPFW

## Slide 22: The IPFW/Army CMS’s Networking Subsystem: Failed iBoot Configuration at RIA Bridge
iBoot's IP address is assigned by the AT&T modem (router) with a dynamic IP address.
To ensure iBoot functional properly, a static IP address and a router with port forwarding function, but current AT&T modem (router) does not met either one of those requirement

## Slide 23: The IPFW/Army CMS’s Networking Subsystem: Failed iBoot with LogMeIn Hamachi Configuration at RIA Bridge
iBoot with LogMeIn Hamachi VPN – SaaS Cloud service
Assigned a virtual IP address to the CMS which is different than the physical IP address assigned by the router.
Failed

## Slide 24: The IPFW/Army CMS’s Networking Subsystem: Tested OK with Wake-On-LAN (WOL) Technology using Magic Packet Configuration at IPFW
But Failed at RIA site
A static IP is required

## Slide 25: The IPFW/Army CMS’s Networking Subsystem: Problems and Tested Solution
Solution Item | Status | Result
Hamachi Virtual VPN software | Tried | Failed due to not able to assign IP to iBoot
iBoot Utility Manager | installed | Successfully installed utility manager, but failed due to no static IP

## Slide 26: The IPFW/Army CMS: Second Problem - Unreliable DSL Service
It was found that CMS Data Server was running normally since our previous maintenance work. The logged data with time stamps shows that the Windows XP Embedded was function properly.
Further investigation showed that was the communication failure instead of the system failure. The connection between the AT&T DSL modem and the Linksys 4 port switch was lost therefore all the communication from outside to the CMS had been lost.
2nd maintenance and patched work at the RIA bridge on July 11-12, 2013

## Slide 27: The IPFW/Army CMS: Second Problem - Unreliable DSL Service

## Slide 28: The IPFW/Army CMS: Solution 1 for Unreliable DSL Service
Reroute Internet connection through a 10 dBi wireless WiFi booster antenna and two routers
One works as transmitter, another serves as receiver
Tried but not implemented due to the access control rights to the AT&T DSL router

## Slide 29: The IPFW/Army CMS: Solution 2 for Unreliable DSL Service
Added a WiFi Hotspot, with AC cooling fan with a thermostat, connected through 3G cellular network

## Slide 30: The IPFW/Army CMS Communication Subsystem: Problem 3 – Unstable WiFi Hotspot
Implemented and running OK for almost a month; communication was lost again on Aug. 16, 2013

## Slide 31: The IPFW/Army CMS Communication Subsystem: Solution to Unstable WiFi Hotspot
Two WiFi hotspots and two USB WiFi adapters were installed and configured.
The system has been running continuously for over two months.

## Slide 32: IPFW/Army CMS Communication Subsystem: Additional Improvement in Progress
Improved RS-485 communication between local sensor data nodes to data server through a Zigbee-based Mash Network (Xbee and Arduino microcontroller board

## Slide 33: Conclusion
Unreliable networking and communication issues with dynamic IP
Real world solutions implemented
  Support or enable remote Internet-based on/off control of the Windows XP-based embedded data server computer
  Two WiFi Hotspots to support Internet networking and communication without static IP address
Future improvement
  Add a ZigBee-based Mash network and extra DAQs to Improved RS-485 communication reliability and sensor node redundancy