## Slide 1: Auto Lynk OBD-II Scanner
Chris Frey
May 3, 2013
ECET - CPET 491 Senior Design Project Phase II
Project Advisor and Instructor: Professor Paul I. Lin

## Slide 2: Summary
Goals
Motivation
Introduction
Problem Statement / Solution
Project Research
Overall Project Design
Hardware Interface
Software Design
Testing and Integration
Project Management
Conclusion

## Slide 3: Goals
On-Board Diagnostic-II (OBD-II) scanner.
  Android-based
  Connection to an OBD-II Bluetooth adapter
  Monitor various vehicle subsystems.
  Users able to identify problems with their vehicles.

## Slide 4: Motivation
Conquer my fear of programming
Interest in smartphones
Interest in automotive systems
Combining these = success?

## Slide 5: Introduction
History of On-Board Diagnostics
  1950’s - Problems diagnosed by hand
  1960’s - Vehicles became more complex
    Humans being removed from the loop
  1980’s - Emerging emission standards
    Malfunction Indicator Lamp (MIL) became required
  1987 - California required OBD-I

## Slide 6: OBD-II
Vehicles produced after 1996
Monitors various vehicle subsystems (Body, Powertrain, Chassis, Network)
  Values such as:
    Engine Load, Oxygen Sensor Voltage, MPH, RPM
Diagnostic Trouble Code (DTC)
  Stored when MIL illuminates

## Slide 7: Problem / Solution
How do we read OBD-II data?
Where do we access it?
Answer:
  Adapter
  Application that allows OBD-II data to be read on a smartphone.
  Reset DTCs when vehicle problem has been solved

## Slide 8: Project Research
OBD-II Specifications
  Standardized hardware interface
  Presented in C/C++ programming language
  Parameter ID (PID) message is sent to the vehicles Engine Control Unit (ECU)
  Value returned in hexadecimal format

## Slide 9: OBD-II Specifications (cont.)
PID | Description | Min Value | Max Value | Units | Formula
04 | Engine Load | 0 | 100 | % | A * 100 / 255
05 | Engine Coolant Temperature | -40 | 215 | °C | A - 40
06 | Fuel Trim Bank 1 Sensor 1 | -100 | 99.22 | % | (A-128) * 100/128
07 | Fuel Trim Bank 1 Sensor 2 | -100 | 99.22 | % | (A-128) * 100/128
0B | Intake Manifold Pressure | 0 | 255 | kPa | A
0C | RPM | 0 | 16,383.75 | Rpm | (A*256) / 4
0D | Speed | 0 | 255 | Km/h | A
0E | Timing Advance | -64 | 63.5 | ° | A/2 - 64
0F | Intake Air Temperature | -40 | 215 | °F/°C | A – 40
11 | Throttle Position | 0 | 100 | % | A*100/255
14 | Oxygen Sensor Bank 1 Sensor 1 | 0 | 1.275 | Volts | A/200
15 | Oxygen Sensor Bank 1 Sensor 2 | 0 | 1.275 | Volts | A/200
AT RV | Voltage | 0 | 15 | Volts | A

## Slide 10: Initial Testing (Termite)
Coolant Temp: 80 (hex) = 128(decimal)
Engine RPM: 0B (hex) = 11 (decimal)
Vehicle Speed: 00 (hex) = 00 (decimal)

## Slide 11: Initial Testing (cont.)
Engine Coolant Temp
A – 40 = (128 - 40) = 88°C = 190°F
Vehicle Speed
A = 0 km/h = 0 MPH
Engine RPM
(A * 256) / 4 = ((11) * 256) / 4 = 704 RPM

## Slide 12: Overall Project Design

## Slide 13: Hardware Interface
Soliport ELM 327 OBDII Bluetooth Adapter
  Allows communication between OBD-II port and smartphone via Bluetooth
  Bluetooth Serial Port Profile
    Emulates RS-232
  Sends and receives ASCII values
  Services one command at a
  time

## Slide 14: Auto Lynk Design
Simple and easy to use
  List format
  Everything on one screen
Meets Requirements
  Reads OBD-II data
  Bluetooth Connectivity

## Slide 15: Auto Lynk Design

## Slide 16: Auto Lynk Algorithm
Establish constant data flow between ECU and Android device
Uses Java Switch statement

## Slide 17: Auto Lynk – The Code
Eclipse IDE
Android Software Development Kit (SDK)
Android Virtual Device (AVD)

## Slide 18: BluetoothChat Example
Enables Bluetooth
Scans for nearby Bluetooth devices
Connects to a Bluetooth device
  Creates socket to communicate between 2 devices
Modified Universally Unique Identifier (UUID)

## Slide 19: Sending Requests to the ECU
Start Transmission with “01 00” message
getData() method

## Slide 20: Parsing the Incoming Data
Regular Expressions
Switch Statement

## Slide 21: Resetting Trouble Codes
Easiest to implement
clearCodes() method

## Slide 22: Testing and Integration
(A * 256)/4 = ((18) * 256) / 4 = 1152
12(hex) = 18 (decimal)

## Slide 23: Testing and Integration (cont.)

## Slide 24: Validation of Requirements
Most requirements validated in demo

## Slide 25: Validation of Requirements (cont.)
Diagnostic Trouble Code Reader
  Deadline approaching
  Code more difficult than expected
    Sheer number of codes
Will be implemented in future

## Slide 26: Bill of Materials
Description | Supplier | Price
Soliport ELM 327 OBD-II Bluetooth Adapter | www.amazon.com | $22.43
RocketFish Micro Bluetooth Adapter | Best Buy | $20.00
Window 7 PC | Myself | $0.00
Java SE Development Kit (JDK) 6 | www.oracle.com | $0.00
Android Software Development Kit (SDK) Includes: Eclipse ADT plugin Android SDK tools Android Platform-tools | developer.android.com/sdk/index.html | $0.00
Samsung Galaxy Nexus smartphone w/ Android 4.2.2 | Myself | $0.00
 | Total | $42.43

## Slide 27: Work Breakdown
Tasks | Estimated Hours of Completion | Actual Hours
System Design | 30 | 40
Assembly Phase | 58 | 77
System Testing | 35 | 35
Final Report Development | 15 | 32
Presentation Development | 10 | 7
Total | 150 | 191

## Slide 28: Schedule
System Design Completed – February 18, 2013
  Research
Assembly Phase Completed – April 3, 2013
  Write Auto Lynk
System Integration Completed – April 25, 2013
  Testing
Final Report Complete – May 2, 2013
Presentation Complete – May 3, 2013

## Slide 29: Lessons Learned
Time Constraints are crucial
Attention to detail
Organizational skills
OBD-II
Programming fear conquered!!

## Slide 30: Conclusion
Provided research for OBD-II and Android
Auto Lynk OBD-II Scanning system was successful, although not complete
More features to be added in future
  DTC reader
  Others

## Slide 31
Questions??

## Slide 32: Demo